## Slide 1: Paper Presentation
achieve0410@gmail.com

## Slide 2: Intelligent Driving Data Recorder in Smartphone Using Deep Neural Network-Based Speedometer and Scene Understanding

## Slide 3: Context
Context
  Introduction
  Speed estimation from gyroscope and accelerometer
  Road facility detection
  Experimental results
  Conclusions and future work

## Slide 4: Ⅰ. Introduction
The driving data recording system are used to store
relevant driving data and provide feedback on driver behavior.
Current DDRs have
  Global Navigation Satellite System(GNSS) receiver
  Accelerometer
  Camera

## Slide 5: Ⅰ. Introduction
DDR’s problems
  High cost
  Lots of useless data
Solution
  Using Smartphone
    Essential devices in the lives – High ownership rate(77%)
    Contained the necessary sensors for developing DDRs
    such as camera, GPS receiver, accelerometer, gyroscope
    Increases the computing power of CPU, GPU

## Slide 6: Ⅰ. Introduction
Significant information for analyzing the driving behaviors
  Position
  Acceleration
  Angle rate
  Speed information
Why speed information is important?
  Road speed limits are legally used in most countries
  The risk of being involved in an accident as a result of excess speed

## Slide 7: Ⅰ. Introduction
Several ways to obtain the speed information
  CAN(Control Area Network)
    Needs to develop the specific interface hardware for accessing to CAN data
    Needs to Consider compatibility
  GNSS(Global Navigation Satellite System)
    Multipath reflection and blockage of GPS signal
      Decrease the accuracy of the speed estimation
    Can be lost in certain areas( e.g. city with tall buildings or under bridges )
    Other methods should be developed as the supplement

## Slide 8: Ⅰ. Introduction
Instead of CAN and GNSS
  Estimated by accelerometer in the vehicle
    Integrating the data from accelerometer using the trapezoidal method
    High accuracy at row speeds and short distance
    but error accumulation may happen for the long distances
  Estimated by accelerometer and gyroscope in the smartphone
    Reset the estimated speed when such situations happen like stopping
    Integrated for detecting reference situations and estimating speed
    Not robust

## Slide 9: Ⅰ. Introduction
Vision based object detection
  Detection of road facilities and objects in traffic scene
  Using Convolutional neural network (CNN)
    R-CNN, Fast R-CNN, Faster R-CNN, YOLO, SSD
    Unable to achieve an acceptable processing time on the smartphone

## Slide 10: Ⅰ. Introduction
Summary
  Using Deep learning based speed estimation method
  Using Lightweight architecture CNN

## Slide 11: Ⅱ. Speed estimation from gyroscope and accelerometer
RNN( Recurrent neural networks )
  Modeling for sequence data
  Vanishing Gradient Problem
3
2
1
5
1
6
23
3*5 + 2*1 + 1*6

## Slide 12: Ⅱ. Speed estimation from gyroscope and accelerometer
Forget gate
Input gate
Output gate
LSTM Network ( Long Short-Term Memory )
  Recurrent neural networks(=RNN) equipped with a special gating mechanism
Each gate has the value between 0 and 1
=> Adjust influence

## Slide 13: Ⅱ. Speed estimation from gyroscope and accelerometer
Concatenated Double-Layered LSTM for Speed Estimation
  Two considered point
    How to build the correspondence between the sequence data and estimated speed

## Slide 14: Ⅱ. Speed estimation from gyroscope and accelerometer
Concatenated Double-Layered LSTM for Speed Estimation
Features of raw data
( In this paper, 128ea )

## Slide 15: Ⅲ. Road facility detection
CNN(Convolutional neural network)
  For object detection
  Well-known deep CNN based detection algorithm
    Faster R-CNN
    YOLO
    SSD
  Depth-wise separable convolution

## Slide 16: Ⅲ. Road facility detection
Standard convolution VS Depth-wise separable convolution
Computational complexity
Computational complexity
ratio
depth-wise convolution
pointwise convolution

## Slide 17: Ⅲ. Road facility detection
Light and Multiscale detection network
  Primary structure is mainly inspired by SSD
  Using depth-wise separable convolution
  instead of the standard convolution
  Fixed-size collection of bounding boxes
  Non-Maximum suppression step

## Slide 18: Ⅲ. Road facility detection
Light and Multiscale detection network
  Problem
    The sizes of detected objects differ
      traffic light, crosswalk
      Solution : Multiscale feature maps
    The shapes of detected objects differ
      Solution : Defines the several default boxes with different aspect ratios
Shallow layers; for traffic lights
Other deeper layer;
for crosswalk

## Slide 19: Ⅲ. Road facility detection
New loss function
SSD’s loss
proposed loss
used to detect
road facilities from the background
used to recognize
the difference among the road facilities

## Slide 20: Ⅳ. Experimental results
Acceleration and angular velocity : Motion sensor in smartphone
Images : Camera in smartphone
Evaluation : GNSS receiver and CAN data recorder

## Slide 21: Ⅳ. Experimental results
Evaluation of Speed Estimation Function
  Used about 50-hours driving data
    45-hours in urban area, 5-hours in National Highway
  Three different locations
    Hitotsubashi, 5km
    Shinjuku, 10km
    Normal road under viaduct
    in Tokyo, 20km

## Slide 22: Ⅳ. Experimental results
Evaluation of Speed Estimation Function
  Result
* WLS-GNSS : Weighted Least Squares GNSS
* Integration Method : proposed by Fazeen et al.

## Slide 23: Ⅳ. Experimental results
Evaluation of Speed Estimation Function
WLS-GNSS has the huge error
: signal blockage and reflection
Integration method shows the error accumulation problem
: especially for the long distance

## Slide 24: Ⅳ. Experimental results
Evaluation of Road Facility Detection
  Focus on the road facilities of intersection areas
    traffic light, stop line, crosswalk
  For developing the road facility detection function
    Label 70 image sequences for training and test
  Follow PASCAL protocol to evaluate the proposed detection network
  Considered as correct when overlap region
  between detection and ground truth is over than 50%

## Slide 25: Ⅳ. Experimental results
Evaluation of Road Facility Detection
  Result
Can achieve 2FPS in the smartphone

## Slide 26: Ⅴ. Conclusions and future work
Conclusion
  Consists of two parts
    Using LSTM neural network based model to estimate vehicle speed
    Using CNN to detect traffic lights, crosswalks, stop lines
  In the future, dynamic object detection will be included